## Slide 1: BreakingPoint Tcl Training
Version 2.0
TM

## Slide 2: BreakingPoint Resources
BreakingPoint User Guide
  Includes Tcl User Guide (171 pages)
BreakingPoint Website – http://www.breakingpoint.com
  White Papers
  Methodologies
  Blog Posts
  Webcasts
  Documentation
  Operating System and ATI (Strikepack) updates

## Slide 3: BreakingPoint Tcl Shell

## Slide 4: Run a Preconfigured Test Case
Goal:
  Run an existing test case using the BPS Tcl API
  Export the Test Report
  Export the data in the packet capture buffer to a PCAP file
BPS Test Case and Tcl Script:
  STBU Strike Level 2
  run_strike_test.tcl
BPS Tcl API Commands:
  set bps [bps::connect $host $user $password]
  set test [$bps createTest –template $bps_testcase –name $new_testcase]
  $bps run –progress “bps::textprogress stdout”
  set chassis_mgmt [$bps getChassis onsystemerror reportSysError]
  $chassis_mgmt exportPacketTrace “C:\temp” 1 0 both
  $test exportReport –file $filename –format pdf

## Slide 5: Modify and Run an Application Traffic Test Case
Goal:
  Load an existing test case using the BPS Tcl API
  Modify and save the application profile
  Assign the modified application profile and save the modified test case
  Run the test case
BPS Test Case and Tcl Script:
  STBU Application Profile
  run _profile_bps_test.tcl
BPS Tcl API Commands:
  set bps [bps::connect $host $user $password]
  set test [$bps createTest –template $bps_testcase –name $new_testcase]
  set app_profile [$bps createAppProfile -template $old_app_profile \
  –name $modified_app_profile]
  $app_profile getSuperflows
  $app_profile removeSuperflow $bad_superflow
  $app_profile addSuperflow $good_superflow 100
  $app_profile save –name $modified_app_profile
  set comp [dict get [$test getComponents] appsim_1]
  $comp configure -profile $modified_app_profile
  $test save
  $bps run –progress “bps::textprogress stdout”

## Slide 6: Modify and Run a Session Sender Test Case
Goal:
  Load an existing test case using the BPS Tcl API
  Modify and save the test case
  Run the test case
BPS Test Case and Tcl Script:
  STBU Session Sender
  run_session_test.tcl
BPS Tcl API Commands:
  set bps [bps::connect $host $user $password]
  set test [$bps createTest –template $bps_testcase –name $new_testcase]
  set comp [dict get [$test getComponents] sessionsender_1]
  $comp configure -sessions.maxPerSecond $new_cps_rate
  $comp configure -sessions.max $new_max_concurrent_connections
  $test save -force
  $bps run –progress “bps::textprogress stdout”

## Slide 7: Create and Run a Custom Strike Test Case
Goal:
  Load an existing test case using the BPS Tcl API
  Modify and save the test case
  Run the test case
BPS Test Case and Tcl Script:
  STBU Custom Strike
  run_custom_strike_test.tcl
BPS Tcl API Commands:
  set bps [bps::connect $host $user $password]
  set test [$bps createTest –template $bps_testcase –name $new_testcase]
  set strikelist [$bps createStrikeList –name $strike_name]
  $strikelist setStrikesFromQuery {aol OR dos OR firefox}
  $strikelist save -force
  set comp [dict get [$test getComponents] security_1]
  $comp configure -attackPlan $new_strike_name
  $comp configure –attackPlanIterations 100
  $comp configure –attackProfile {}
  $test save –force
  $bps run –progress “bps::textprogress stdout”

## Slide 8: Create and Run a RFC 2544 Test Case
Goal:
  Create a RFC 2544 test case using the BPS Tcl API
  Modify the test case
  Run the test case
Tcl Script:
  run_2544_test.tcl
BPS Tcl API Commands:
  set bps [bps::connect $host $user $password]
  set test [$bps createRFC2544Test]
  $test configure –packetType Ether
  $test configure -customSteps {64, 512, 1024, 1380, 1518}
  $test run –progress “bps::textprogress stdout”

## Slide 9: BreakingPoint Q & A
Mike Murphy – mmurphy@breakingpoint.com
Roy Scaife – rscaife@breakingpoint.com
BreakingPoint Webpage – http://wwwin-people.cisco.com/mikemur/
BreakingPoint Support – email: support@bpointsys.com
phone: 1-866-352-6691 extn 4
Thank you!